## Slide 1
History of OMRON prox.
--- Transition of technology for prox.---
The proximity switch is the traditional business in OMRON which was developed and released in 1960 and has been accumulated for 43 years since that.
Our proximity sensor business has grown the No.1 volume production in the world,
and we are still working for the NEW technology of proximity sensors .
By this significance, the history of OMRON proximity sensor is also the history of the proximity sensor in the world.
SKN Kenji Ueda
Arranged : Kazushi Tanase
Mar. 2005 OEE SenBU KT

## Slide 2
1. History of OMRON prox products
1960 70 80 90 2000
Square type
Cylindrical type (M08 to M30)
Long sending distance with big shape type
Small dia. Cylindrical (dia. 4mm to M05)
Separate amp. type
Shape of sensor
Genesis stage
Infancy stage
Growing stage
Mature stage
U-slot type
Slot type
Ring type
Square & robust type
Slim & Flat square type
Square type
Small square type
Cable with amp. type
U-slot type
Slot type
Separate amp type
Mar. 2005 OEE SenBU KT

## Slide 3
Si transistor
X0.7 Sn
(only non shielded type)
1960 70 80 90 2000
Original IC
DC 2 wire
AC 2 wire
Stable operation indicator
Ge transistor
Discreet chip mounting
Sensitivity
Electrical circuit technology
Chip mounting technology
DC3 wire (PNP)
Operation indicator
SMT
COB (Chip on board technology)
DC3 wire (NPN)
DC3 wire (NPN, PNP)
AC/DC 2 wire
X1.0 (CENELEC standard)
Long Sn X1.5
X0.5 CENELEC Sn (only non-shielded type
Double Sn X2.0
Short circuit protection (standard function for DC type)
History of OMRON prox technology
Non-polar DC2 wire
Genesis stage
Infancy stage
Growing stage
Mature stage
Mar. 2005 OEE SenBU KT

## Slide 4
2. History of OMRON proximity sensor
1960 | TL-1G,1H TL-2G,2H | - Invention of proximity sensor (Ge transistor & PNP voltage output) - -1: all metal , -2: for ferrous metal - G,H : Sn=4mm , 8mm Case material : Aluminium
1961 | TL-2GP,-2HP -A, -A31, -A32 | - Current output type - Square, U-slot and ring type
1962 | TL-1VN, 2VN TL-3FC, 3HC, 3GC | - Sn 16mm type - Separate amp type for non-ferrous metal detection
1963 | TLF TLB | - Floating metal detection type for liquid level detection. - Capacitive proximity sensor
1964 | YL-2GP-A | - AC 3 wire type
1966 | TL-1FN, 2FN, 2FN-A53 | - Slot shape type - Micro switch compatible shape type
1967 | TL-H1VC | - Separate amp type for high ambient temp.
1968 | GL | - lead switch principle type (magnetic proximity sensor)
1969 | TL-S YL-S | - Change from Ge transistor to Si transistor for all prox. Changed from PNP to NPN output in this term. In those days, it’s possible to make only NPN transistor.
<1960‘s Genesis stage>
Mar. 2005 OEE SenBU KT

## Slide 5
1970 | TL-N5, N10, N20 TL-H10, H20 TL-A5, A10, A20, A20H TL-K5, K10 TL-Y10 TL-L100 TL-U | - Full model change with using Si transistor Standardization of the shape and characteristics (Square & Ring type) - Separate amp type for all metal detection -A type: common use -K type : for machine tool & high resolution -AC 3 wire - Long sensing distance by differential coil operation type. Sn=100mm - Only ferrous metal detection type ( detect ferrous metal behind non-ferrous metal)
1971 | Establishment the operation analyze method of high frequency oscillation type proximity sensors. | Establishment the operation analyze method of inductive prox. 2 terminal circuit calculation method was adopted for prox.
1972 | TL-N-N, PN-N TL-I | - Include the operation indicator - Sensor for hazardous gas areas.
1973 | TL-F20, TL-G3 | - Renewal the U-slot shape type and Slot shape type
1974 | TL-X, -XP | - Cylindrical shielded type prox. Germany maker preceded on the shielded type. - Constitute the CENELEC standard
1975 | E2M series | - Limit switch compatible shape (aluminum die casting case) - Original IC for power supply and output circuit
1978 | TL-LP50, LY50 E2K-C25 | - High robust type for heavy industry Sn=50mm - Capacitive proximity sensor (smooth barrel cylindrical)
1979 | New TL-X series | - Down sizing and high performance on cylindrical type Original IC for whole circuit of prox. Vacuum resin filling process COB (Chip On Board) technology
<1970‘s Infancy stage>
Mar. 2005 OEE SenBU KT

## Slide 6
198１ | TL-M E2P TL-X-50 | - Micro switch compatible shape - Limit switch compatible shape (for GM, FORD corp.) (Varikont type to change sensing face for 4 directions) -Special cylindrical prox. For GM, FORD corp. (incl. Weld Field Immunity type)
1982 | TL-XD TL-N-N series E2K-X series | - DC2W cylindrical prox (discreet chip circuit) - Renewal TL-N series (adopt IC chip) - Capacitive proximity sensor (threaded barrel cylindrical)
1973 | E2C TL-W, TL-T | - Renewal separate amp type - Flat shape, Slim shape type
1984 | E2CA E2EQ E2K-F | - Analog output prox with separate amp. - Varikont type ( to change sensing face for 5 directions) - Flat shape capacitive proximity switch
1985 | E2E E2F | - Full model change of TL-X series - Plastic threaded cylindrical type
1986 | E2EC E2C-J E2EZ | - Small dia cylindrical type with cable and amp - Small size Amp for separate amp type (E2C) - Special type that don’t detect non-ferrous metal cut pieces
1987 | E2E-XD-N F2LP | - Line up DC2W type to E2E series Original IC for DC2W type Sn=CENELEC x 1.5, Stable indicator - Small passing metal detection sensor
<1980‘s Growing stage>
Mar. 2005 OEE SenBU KT

## Slide 7
1990 | E2EV | - All metal detection sensor
1991 | E2EY E2J | - Only non-ferrous metal detection sensor - Capacitive sensor with separated amp.
1992 | E2CD | High resolution prox with separated amp. (temperature drift learning function)
1995 | E2C-T | - Separate amp type with Sn teaching functions
1996 | E2E-X?X E2E-X?T | - AC/DC 2 wire type - non-polar DC2wire type E2E DC2 wire type was awarded “Energy-Conserving Machinery “ from JMF (Japan Machinery Federation)
1998 | E2S | - Small square shape type
1999 | E2EM E2ES | - Long sensing distance prox (CENELEC x 2 Sn) - SUS metal sensing face type
2000 | E2K-L | - Capacitive sensor for liquid level detecting
2003 | E2A | Long sensing distance prox (CENELEC x 2 Sn) (Full line-UP) (realize with modulated structure)
<1990‘s Mature stage>
Mar. 2005 OEE SenBU KT