## Slide 1
Magnetic field control technology
E2A has unique technology to control the magnetic fields from inductive sensors.
The copper ring which is mounted in beside of sensing surface is controlling the shape of magnetic fields. And this magnetic fields were optimized by design of ring material, shape and position.
We have several PAT for this technology as unique method for longer sensing distance type.
Sep. 2005 OEE SenBU KT

## Slide 2
Sep. 2005 OEE SenBU KT
no-ring no-case
no-case
In case of there are no ring and metal case, the magnetic flux is expanded and reach more to target.
High sensitivity
But big influence of surrounding metal
Metal case
Target
Ring
In case of there are a ring beside of ferrite core, the magnetic fields are formed and not crossed in metal case area.
Reduced sensitivity
No influence of surrounding metal
Ferrite core
In case of metal case is installed, almost no change in magnetic fields shape.
 No effect from metal case for sensing distance.

## Slide 3
Sep. 2005 OEE SenBU KT
The purpose of ring is …
Reduction of influence of metal case material.
Reduction of influence of surrounding metal.
Fast modification for customer
Reduction of number of parts  cost down
Better usability
The magnetic field of E2A has been optimized
for sensing characteristics,
for less surrounding metal influence.