## Slide 1
High reliability for temperature stress……
Keep the high reliability policy of OMRON Proximity sensors.

## Slide 2
Confidential
1 hour
Hot air : +85degC
Cold air : -40degC
1 hour
Heat shock test
1. –40degC 1 hour
2. +85degC 1 hour
3. Measure the insulating resistance and dielectric voltage
4. Measure the Sr.
5. Repeat from 1 to 4 process.
Criteria
1)Drift of Sr should be less than 10%.
2) Insulation resistance should be more than 10M ohm.
( measured by 500VDC)
3) Dielectric strength should be more than 1000V.
(1000V / 1 minute Leakage current should <1 mA )
Heat shock test
E2A have high performance same as E2EG.
Repeat cycle (times)
300
200
E2A
E2EG
100
Keyence EV
M18 shielded type
100
More than 300
YAMATAKE FL7M
100
IFM IGB
P+F ＮＢＢ５
300
Reduce the stress of filled resin !
And E2A is optimized the inner stress by using the 3D-simulator.
More than 300
More than 300

## Slide 3
M12 shield WP type
M12 shield M1 type
Confidential