## Slide 1
Product concept for E2A ……
New proximity sensor ……
Module concept…
Lower cost ….
Short lead time ….
Individual design
Module combination

## Slide 2
Shorter delivery time for customization
High reliability
of customization
High cost-effective
1) Products consist of 4 module
Individual design
Module combination
2) Sensing spec is depend on only Sensing module.
Full automatic process for sensing module
Reduction the variety of parts
Reduction the variety of sensing module
Reduction the parts control cost
Old concept
New concept
Benefit for Customer
1) Each parts for each design

## Slide 3
- Cable； 2m, 5m, 10m length
Robot ,
（PUR Halone-free）
- pig tail
Connection module
・ＤＣ２Ｗ
ＮＯ、ＮＣ、non-polarity
・ＤＣ３Ｗ
ＮＯ、ＮＣ、ＰＮＰ、ＮＰＮ、
Voltage output, Open collector
・ＡＣ２Ｗ
・ＡＣＤＣ２Ｗ
Out put module
・Brass barrel； Short body
Long body
・Stainless barrel
・Teflon coating barrel
・Teflon barrel
・Plastic barrel
Body module
-Distance range
x1, x2, x3(plan)
-Different frequency
-Teflon coating face
Sensing module
Flexible Combination

## Slide 4
Coil case
Spool
Ferrite core
Sensing ＩＣ、ＰＷＢ
FPC
Base metal case
( Brass, SUS )
Cable clump
Cable protector
cable
Sensing Module
E2A Technology Innovation
OUTPIUT ＩＣ、ＰＷＢ
Winded shield
Filling resin
Optimized shape
Less effect of base metal case
High accuracy assembly
Lower cost noise shield
Sensing spec is depend on only Sensing module.

## Slide 5
■ Environment
■ Improve the water-proof
Points
1. Take a long distance of water-invasion route
2. New material bonds the plastic and cable.
The product-tail design change the structure and materials.
Reduce the lead metal
Reduce the collision by objective target
E2A Explanation
Product designed by
Magnetic-field Simulation
M8 ； 1.5 → 2 mm
M12； 2 → 4 mm
M18； 5 → 8 mm
M30； 10 → 15 mm
Eliminate
Bisfenol-A
CSP
mount
Final assembly
by workers
Sensor module production
by Automatic machine
Module stock
400
1200
mg
Lead metal
Existing
E2E□
New E2A
Comp.
prod
barrel
cable
solder
Final assembly does not need
large amount of investments.
Developing the triple distance
■ Double distance
■ Production