## Slide 1
Magnetic field immunity of E2A
DC magnetic field………
AC magnetic field………
100 to 200 gauss is limit
10 to 100 gauss is limit
E2E(G) has higher magnetic field resistance than E2A!!
(Please ask to OEE SenBU for detail data)
confidential
Mar. 2005 OEE SenBU KT

## Slide 2
confidential
Do not provide this paper to customer!!
DC magnetic field immunity
Value in ( ) shows sensing distance compared with IEC standard.
Mar. 2005 OEE SenBU KT

## Slide 3
AC magnetic field immunity
confidential
Do not provide this paper to customer!!
Value in ( ) shows sensing distance compared with IEC standard.
Mar. 2005 OEE SenBU KT

## Slide 4
Magnetic field calculation near high current line.
I [A]
High current wire.
a [m]
Point A
How much magnetic field at point A?
Magnetic field B=(2*10-3*I)/(a) [gauss]
In case of DC current!!
This value is changed by surrounding metal of high current wire.
We recommend to do sample test at real applications!!
Mar. 2005 OEE SenBU KT

## Slide 5
Magnetic flux resistance  depend on rotation position of sensor.
sensor
Magnetic flux direction A
Magnetic flux direction B
Magnetic flux direction A and B cause different resistance level.
This came from shape of ferrite core in sensor.
If you had malfunction signal in magnetic field,
You can try to turn the sensor into good direction!!
Mar. 2005 OEE SenBU KT