## Slide 1
High water-proof construction ……
High reliability for harsh applications …
By special structure in cable protector.

## Slide 2
E2EG
Point
1) Increase a distance of water-proof destruction.
2) Increase a adhesive strength between each materials.
3) Cable protector keep high adhesive force with cable.
・more than 3 times for creeping distance.
red line  adhesive point → extend this root.
blue line  no-adhesive point (water can go through)
E2A
Change the material of protector: Nylon  Polyester elastomer
(good adhesive strength)
Process for protector:
 Molding process
( Reduce the assembly struggling)
New structure
for high water-proof
1)
2)
3)
1)
2)
3)

## Slide 3
Criterion
1) Drift of Sr should be less than 10%.
2) Insulation resistance should be more than 10M ohm.
( measured by 500VDC)
3) Dielectric strength should be more than 1000V.
(1000V / 1 minute Leakage current should <1 mA )
Confidential
Under water
30 minute
Hot water :
70 degC
Cold water :
0 to 5 degC
Under water
30 minute
Water-proof test
(temperature shock)
<Information>
IP67
(IEC60529 standard)
1m
Increase the water-proof performance
・ E2A pass the more harsh test than IEC standard (IP67).
・ by new structure on cable protector
＊Our original test (to simulate the real application)
Repeat cycle (times)
100
50
E2A
E2EG
5
Keyence
M18 shielded type
More than 100
YAMATAKE
50
IFM
P+F
5
More than 100
More than 100
30 minute