## Slide 1
Connector rotation torque of E2A?
M8 size CN (E2A-**-M3/5-**)
M12 size CN (E2A-**-M1-**)
Please fasten the connector by >1.5 Nm
Sep. 2005 OEE SenBU KT
Please fasten the connector by >0.3 Nm

## Slide 2
Test result of connector rotation torque
Type of connector | Rotation torque | Function break torque
M12size | 0.6 Nm | 0.8 to 0.9 Nm
M8 size (M8 body) | 0.3 Nm | Whole inner rotate (M8body)
Sep. 2005 OEE SenBU KT
Type of connector | Rotation torque | Function break torque
M12size special version | 1.2 Nm | 1.6 Nm
Rotate the connector with measuring torque.
Special type to increased connector rotation torque.

## Slide 3
Sep. 2005 OEE SenBU KT
 | OMRON E2A (Brass) | OMRON E2A (SUS) | OMRON E2A Special type | OMRON E2EG | OMRON E2EL | BALLUFFBES M18MD1-P8C12B-S04G | IFM IGS204 (M18) | IFM IFS204 (M12)
No. of samples | 1 | 3 | 4 | 2 | 1 | 1 | 1 | 1
Start Rotation | 0,6 | 0,9 0,9 0,7 | 1.2 | 1,95 -- | 2,4 | 1,1 | 1,3 | 1,0
Break Function | 1,0 | 1,35 1,3 1,3 | 1.6 | 2,7* 2,8* | 3,4* | 2,5 | 1,5 | 1,2
Note) * mark means pin break, not function break.
Comparison data of rotation torque