## Slide 1
Vibration and Shock test of E2A
OMRON has higher test standard than IEC60947-5-2 norm.
Mar. 2005 OEE SenBU KT

## Slide 2
Vibration test
10 to 55Hz, 1mm amplitude,
5min / sweep cycle, 30min in each axis
10 to 2000Hz, 1.5mm amplitude or 15g,
15min / sweep cycle, 150min in each axis
IEC norm
OMRON standard
Vibration generator
E2A
IEC 60947-5-2
Condition near the high speed engine!
Mar. 2005 OEE SenBU KT

## Slide 3
Shock test
Half sine shape pulse, 30g, 11msec,
6 times in each axis
Half sine shape pulse, 100g(1000m/s2), 11msec
10 times in each axis
IEC norm
OMRON standard 1
IEC 60947-5-2
Real application test (OMRON original)
200g, 300000times, at 23 degC
OMRON standard 2
Hammering the mounting bracket
Mar. 2005 OEE SenBU KT