## Slide 1
Sensor Business Unit
Test Criteria for E2A
Many +
from standard norm

## Slide 2
General
General function test
+/- 3 sigma judgment in development
OMRON is evaluating the test result by +/- 3 sigma range.
+/- 3 sigma = 99.7% in range
Each pieces inspection (100%) test
+
Basic function

## Slide 3
Test for inductive sensor E2A
Test Norm for inductive sensor
IEC 60947-5-2
EN 60947-1
Inductive proximity switch norm
IP rate (water proof regulation)
EN 60529
Low voltage equipment
+
OMRON Original test items
OMRON Original test criteria
Experience in Market

## Slide 4
Test for inductive sensor E2A
Ambient temp change
1000 hour at 85degC with max load current
OMRON original
+
Heat shock test
-40 to 85degC each 1h 100cy
85 degC
-40 degC
1 hour
1 hour
Ambient temp

## Slide 5
Test for inductive sensor E2A
Water proof test
IP67: under 1m water 30min
IEC 60529
+
Hot and Cold water cycle
5 to 70degC each 30min 50cy
70 degC
0 to 5 degC
30 minute
30 minute
Ambient temp
IP69K for standard E2A series  E2A = IP67, IP69K

## Slide 6
Test for inductive sensor E2A
Vibration / Shock test
Vibration : 10 to 55Hz, 1mm Amplitude, 5min sweep, 30min each axis.
IEC 60947-5-2
+
OMRON original
Shock : Half sign pulse, 30g acceleration, 11ms pulse, 3 times / axis.
Vibration :
10 to 2000Hz, 1.5mm Amplitude, 15min sweep, 150min each axis.
Shock : (Hammer shock test)
Hitting the mounting bracket of sensor by metal hammer.
200g acceleration, 300,000 times
These original test criteria is based on experience in prox market.

## Slide 7
Test for inductive sensor E2A
Noise immunity test
RFI (3V/m) , FTB (2kV), ESD (4/8kV) , conducted noise immunity (3V)
IEC 60947-5-2
+
OMRON original
RFI (10V/m) , FTB (2kV), ESD (4/8kV) , conducted noise immunity (10V)
Inverter noise test :
Square shape wave common noise  simulated for real inverter noise.
1k to 30kHz: 60Vp-p, 30k to 100kHz: 40Vp-p
Impulse voltage immunity :
1kV (between power line), 1.5kV (common mode), 100 ohm impedance
1k to 30kHz: 60Vp-p, 30k to 100kHz: 40Vp-p
Impulse voltage immunity (1kV, 1,2/50usec, 500 ohm source impedance.
Mobile phone noise immunity :
800MHz, 1.5GHz, 1.9GHz mobile phone  0.2m to sensor
27MHz, 144MHz, 430MHz, 900MHz, 1200MHz transceiver (10W)
 0.2m to sensor
IEC 60947-5-2
Original criteria is simulating the real application conditions.