## Slide 1
Standard E2A can be used at 85degC!!
With limitation of load current and supply voltage
Maximum Ambient Temperature of E2A?
Need test in customer.
Operating temperature
Storage temperature
Hardening Temp : Sensing module  120 degC
Whole sensor  88 degC
Mar. 2005 OEE SenBU KT

## Slide 2
Supply voltage | M8 | M12 | M18 | M30
10 to 30V | 100mA | 200mA | 200mA | 200mA
30 to 32V | 50mA | 50mA | 50mA | 50mA
DC3W (standard type = 200mA)
Maximum Load Current Limitation at 70 to 85 degC
DC2W (standard type = 3 to 100mA)
Supply voltage | M8 | M12 | M18 | M30
10 to 30V | 50mA | 50mA | 100mA | 100mA
30 to 32V | 50mA | 50mA | 50mA | 50mA
For the customized type, please ask to OEE-SenBU.
Mar. 2005 OEE SenBU KT