## Slide 1
Higher EMC type of E2A
Standard E2As already have higher EMC level.
Sep. 2005 OEE SenBU KT
E2AU --- 30V/m RF noise immunity
Some E2A --- 100V/m RF noise immunity
If you still have problem in real application,
We can provide further modified type of E2A.

## Slide 2
Sep. 2005 OEE SenBU KT
Ground plane
Special type
= lower response frequency (10Hz response)
= higher RF noise immunity when noise came in from sensing surface.
Oscillation circuit
Integration circuit
Switching circuit
Output circuit
Special type has higher integration constant = lower response
 Lower sensitivity for disturbance from sensing coil.

## Slide 3
Sep. 2005 OEE SenBU KT
Specifications of higher EMC type
/ low response frequency (10Hz)
/ another specifications are same as standard type.
These type can be realized by RIS request.