## Slide 1
Comparison with TURCK (U-Prox)…..
IFM (m-series)…..
E2A has advantage in reliability for harsh applications.

## Slide 2
IFM m-series (connector type)
Resin free sensor
Calking process to fix the connector parts.
The case of coil is fixed to metal case only by pressing insert.
The coil case may be loosened by “Vibration or Shock”.
Low reliability for vibration or shock.
The water-proof performance depends on only 2-o-ring.
Smaller sealing area.

## Slide 3
Coil wire is connected to PWB directly
X-ray photo
TURCK U-Prox
The resin stress will applied to the coil wire.
Low reliability for
“Heat cycle applications “.
Sensing face
This construction don’t suit for standard Prox. (reliability and cost )
3- coils