## Slide 1
Analysis report of TURCK U-Prox+
Ver 3.0

## Slide 2
Appearance
Remaining of Resin filling Hopper (2 points)
Same as E2A?
LED (1color, Yellow)

## Slide 3
After removing metal case
Metal case (Brass)
/ Rough surface of inside metal case
/ Good adhesiveness between resin and metal case
Coil Case
/ Long length
/ 4 ring on case
Resin
/ Foamed resin
/ Hard but possible to cut by knife

## Slide 4
X-ray analysis
Print Coil
ＬＥＤ
Shield plate

## Slide 5
After remove resin
ＬＥＤ
Shield Ring (brass)
Connected to GND (soldered at 2 points)
Coil Case
There is a kind of evaporated layer inside of coil case. No connection to GND.
Same function with E2A ring??

## Slide 6
After remove resin

## Slide 7
PCB
Print Coil
4 layer PCB, coil on 1st and 4th layer
4 layer PCB
Rectangular coil on 1st 4th layer.
To reduce surrounding metal influence?
IC
TURCK Original
This shape will help better adhesiveness resin and PCB.

## Slide 8
Dimension
63.9mm
60.0mm(metal case)
25.0mm
26.0mm
29.8mm
1.0mm
19.2mm
0.6mm
Thickness of Coil Case
0.5mm
Thickness of Shield ring
3.3mm
Gap from PCB and Shield ring
1.05mm
PCB thick ness
42.0mm
Length of PCB
φ6mm
Cable dia

## Slide 9
Special coating at inside of head cap.
Under plating = Cu + Sn
Surface plating = Ni
Modifying the magnetic flux
 Embedded mounting in ferrous metal.
Same technology as special ring in E2A and E2A3.
Extremely expensive solution !!
No cost competitive with existing technology.

## Slide 10
Sensing distance adjustment
U-Prox+ has been adjusted the sensing distance by laser trimming.
In case of not succeeded to adjust, they add additional register on the trimming resister.
Not suite for mass production.
High cost to adjust the sensing distance.
Print coil could not help to make sensing distance adjustment easy.

## Slide 11
Detecting area
In case of target approach from side of sensor.
Big change of sensing position by flip-flop of target.
In case of target approach from side of sensor.
Big change of sensing position between ferrous and non-ferrous metal.

## Slide 12
Under water
30 minute
Hot water :
70 degC
Cold water :
0 to 5 degC
Under water
30 minute
＊Our original test (to simulate the real application)
Repeat cycle (times)
50
25
E2A
More than 50
TURCK
U-Prox+
3
Water proof test
These points had insulation break.
U-Prox+ does not fit for water proof application.

## Slide 13
Small target detection
U-Prox+ cannot detect small ferrous metal target.
Sensing object = ferrous metal.

## Slide 14
Not possible “recessed mounting in non ferrous metal. –0.5mm  ON
Bigger sensing distance decreasing.
Bigger sensing distance decreasing.
Influence of surrounding metal
Wider sensing area by non-ferrous metal.
Bigger influence from non-ferrous metal.
U-Prox+ : Recessed mounting 0.5mm
Not possible recessed mounting in Alminum!!