## Slide 1
Connector PIN arrangement of E2A?
M12 size CN (M1CN) (DC2W)
IEC compliant (standard in EU)
Japanese type (standard in Toyota, Nissan….)
M8 size CN (M3CN, M5CN)(DC3W)
Only IEC compliant
4pins : M3CN
3pins : M5CN
M12 size CN (M1CN) (DC3,4W)
Only IEC compliant
Mar. 2005 OEE SenBU KT

## Slide 2
M12 size CN (M1CN) (DC3,4W)
IEC compliant (standard in EU)
CN pin No. | DC3W |  | DC4W
 | Normally Open | Normally Close | Antivalent
1 | +V | +V | +V
2 |  | OUT | NC OUT
3 | GND | GND | GND
4 | OUT |  | NO OUT
Mar. 2005 OEE SenBU KT

## Slide 3
M12 size CN (M1CN) (DC2W)
IEC compliant (standard in EU)
CN pin No. | Normally Open | Normally Close
1 | +V | +V
2 |  | GND
3 |  | 
4 | GND | 
Japanese type (standard in Toyota, Nissan….)
CN pin No. | Normally Open | Normally Close
1 |  | 
2 |  | +V
3 | GND | GND
4 | +V | 
Mar. 2005 OEE SenBU KT

## Slide 4
IEC compliant (standard in EU)
CN pin No. | 3pins M5CN | 
 | Normally Open | Normally Close
1 | +V | +V
2 |  | 
3 | GND | GND
4 | OUT | OUT
M8 size CN (M3CN, M5CN) (DC3W)
CN pin No. | 4pins M3CN | 
 | Normally Open | Normally Close
1 | +V | +V
2 |  | OUT
3 | GND | GND
4 | OUT | 
Mar. 2005 OEE SenBU KT